## Slide 1
Notes: SSC: Source Controllers, Source QC, Navigation, Tracking
iSeis: Seismographs, Receiver QC, Data Handling, Noise QC

## Slide 2
Ponca City, Oklahoma – Home of Vibroseis
1953 – 1969 Conoco Oil Developed Vibroseis
1969 – 2001 Pelton Co. operated in Ponca City
2001 – Pelton Co. was purchased by Input/Output
2001 – SSC founded in Ponca City
Seismic Source Company (SSC)
1953 First Vibrator Unit

## Slide 3
Seven Engineers and Managers from Pelton Co. started SSC in 2001
Seismic Source Company
Kim Mitchell
  1965 - 1968 : Conoco Oil
  1969 - 2001 : CEO Pelton Co.
John Giles
  1985 - 2001 : President Pelton Co.
  2001 - Present : President SSC
Kyle Benton: 1990-2001 = Pelton Co., 2001-Present = SSC R & D development
Andras Feszthammer: 1998-2009 = Input/Output, 2009-Present = SSC
Scott Burkholder: 1985-2008 = Lookout Geophysical, 2008 = Present SSC
Vitaly Shevkunov: 1997-2001 = Pelton Co., 2001-Present = SSC

## Slide 4
2001 First Product DAQlink1
  Sold to Exxon Oil for Vibrator Quality Control
2002 - Sold first Boom Box unit ( Dynamite Blasters)
2004 – Sold First BirdDog geophone test system
2005 – Sold first Force 1 Vibrator control System
2010 – Started International Seismic Co.
  Developed Sigma Nodal Recording system
Seismic Source Company

## Slide 5
Seismic Source Company
2012 First Force 3 Vibrator controller sold
2013 First BoomBox 3 (Dynamite Blaster)
2015 Inova purchases first VibPro HD system
2017 Inova purchases first ShotPro HD system

## Slide 6
Seismographs
  Over 25,000 channels world wide
  Includes DAQlink and Sigma
Source Controllers
  Universal Encoder 2
  Boom Box 3 – over 2500 units sold
  Force 3 Vibrator controllers
  RTM 3 Weight Drop Controllers
Bird Dog 3 Field QC Systems
  Geophone Testing
  Hydrophone Testing
  Vibrator Quality Control
Seismic Source Company

## Slide 7
Latest Generation of Source Controllers and Acquisition Management Software
Designed for High-Productivity Acquisition
Universal Compatible
The most advanced and versatile source control solution on the market
Force 3 Source Controllers

## Slide 8: Source Link
Designed for High-Productivity Acquisition
Compatibility with most data acquisition systems
The most advanced and versatile source control solution on the market

## Slide 9: SourceLink = Universal Control System
SourceLink

## Slide 10: Recording System Support
iSeis Sigma
Wireless Seismic
GTI
Smart Solo
InnoSeis
INOVA Quantum
Fairfield Nodal
Geospace
Global AutoSeis
Sercel 408/428/508
Aram

## Slide 11: Multi-Functional Front End
Provides full Data Acquisition front-end functionality for traditional and advanced vibroseis, impulsive and airgun sources
Deployment/Pickup/Node Status support for node acquisition units
Intuitive Source Parameter Management for all supported decoders

## Slide 12: Survey files
All Survey Input standards are supported, such as SEG-P1 and SPS
Basic GPX file support
ESRI Shape files for exclusion zone, roads, pipelines, fence lines, waters, etc.
Satellite Images (GeoTiff, BMP, JPEG, JPEG2000, etc.)
Google Earth
Datum transformation with built-in Global Mapper engine

## Slide 13: User Drill Log
Drill log import support
Configurable to support any input
Depth, charge size, comments
HSE: Allows to mark and warn of hazards

## Slide 14: Full Featured Reports
Full featured Observer log
SPS and SP1 for acquired shots
Source QC reports
Group COG reports
Timebreak reports for the various recording systems

## Slide 15: Supported Source Types
Dynamite
Vibroseis
Weight-drop
Air-gun
Works with all these source types seamlessly in the same project
Dynamite
Shooter
Vibroseis
Fleet

## Slide 16: Traditional Acquisition Methods
Standard vibroseis
  Conventional
  Flip/Flop
  Interleave
High Performace VibroSeis (HPVS)
  Slip-Sweep
  Distance Separated Simultaneous Sweeps (DSSS)
  Distance Separated Simultaneous Sweeps with Slip Sweep (DS4)
  Independent Simultaneous Sweeps (“Free-for-all”) (with full QC)
  HFVS
Standard Dynamite and Weight Drop

## Slide 17: Autonomous Acquisition Methods
Autonomous VibroSeis
  Single or multi vibrator fleets
  Time slice for each group when they can shake
  Timebreak, location and QC stored in decoder units and can be retrieved during production or at the end of the day.
  Semi-realtime automated download over VHF or Wi-Fi

## Slide 18: Autonomous Acquisition Methods
Assisted Autonomous VibroSeis
Vibrators operate independently using the ISS scheme
When out of radio range, the Force Three unit saves the information into its memory
When in radio range, SourceLink downloads the shot and PSS information and displays it to the user

## Slide 19: Autonomous Acquisition Methods
Autonomous Dynamite
  Great for nodal systems
  Alleviates radio dependency
  Easy setup for BoomBox 3 units to program the available time slots for shooting
  Each Boombox 3 can be programmed with source points that are ready to be shot. This ensures that the shooters can’t accidentally shoot source points that have no spread yet
  GPS Location and QC (including uphole signal) is stored in the BB3 memory
  After download, SourceLink creates acquired shot events and shows QC information. Reports and timebreaks can be produced from SourceLink
Standard Dynamite and Weight Drop

## Slide 20: Autonomous Acquisition Methods
Autonomous Weight Drop
  Single weight-drop unit only
  SourceLink runs in the Weight-Drop vehicle’s cab
  User can easily void and redo weak or bad hits when SourceLink is in the cab / truck.

## Slide 21: Fail-Safe Design
Each product saves shot information and QC data in memory
Download via Ethernet or Wi-Fi connection into Source Link
SourceLink populates database and reports can be generated for harvesting and transcribing
All information is stored redundantly in Encoder and Decoders

## Slide 22: Quality Control – Dynamite Operations
  GPS Location
  Timebreak time (microsecond accuracy)
  Uphole signal and time
  Fireline and cap information
  Cap serial number

## Slide 23: Quality Control – VibroSeis Operations
PSS – Phase, Force Distortion
Cross-Correlation Wavelet – Spectrum and Phase
GPS Position – Status and Health of GPS Receiver
GPS Time – Time error from each vib. Compares VHF radio sync and GPS time sync
Vibrator Signature Recording Status – Status sent to central via PSS
Radio Similarities – Comparison of Sim and Loop accelerometers via digital PSS and cross-correlation wavelet
Radio Similarities available for both Analog and Digital radios
PSS Status – Battery and Instrument Voltages
Limits Reached PSS Status – shows if limits have been reached
WiFi Download of Vibrator Signature Data
Wireline Sim Data – via Signature Data – can generate Wireline Sim data for every sweep

## Slide 24: PSS - Traditional QC Display

## Slide 25: PSS – Sortable, Filterable Grid

## Slide 26: PSS – Gant-Chart for QC and Timing analysis

## Slide 27: PSS – Location Based Visualization

## Slide 28: PSS – Location Based Visualization

## Slide 29: PSS – COG QC
Source Position analysis from PSS information
COG calculation
Distance to Source Point

## Slide 30: Source Coordination for Data Acquisition
Group Tracking
Dynamic display for vibrator
position and group COG
Status (Pad up/down, Ready)
Relative distance to source point
Acquisition and sweep details
Abort VP, reject and redo current sweep
Warnings for distance or missing units in receivers

## Slide 31: Shape Files for Exclusion and Buffer Zones
  Import KML or ESRI Shape files
  At import or after import, mark if the polygon represents an exclusion or a low force buffer zone

## Slide 32: Exclusion Zones
  Immediate notification if a vibrator enters an exclusion zone

## Slide 33: Low Force Buffer Zones
  System automatically will use low force if any of the vibrators in the fleet is inside a low force buffer zone

## Slide 34: 3D Google Earth Visualization
SourceLink provides Google Earth based data for offline planning and analysis
Pre-planning
Detours
Daily progress report for management
Source Point status with PSS
Check vibrator trail against no-drive zones
Box location and status

## Slide 35: Spread Overview

## Slide 36: Source Point w/ PSS Info

## Slide 37: Vibrator Trail

## Slide 38: SourceLink + Sercel 408/428/508 & OVC
Integration of SourceLink/UE2/Force3 with a Sercel 408/428/508 recording system using the OVC interface
Enables Observer Driven acquisition in Flip-Flop or Ping-Pong mode with two or more fleets.
Integrated Operation Process:
  User selects Source Point, Active Spread and Vibrator Group in 408/428/508
  Sercel sends fire command to SourceLink and waits for the timebreak
  SourceLink starts Vibrators and sends timebreak and QC to Sercel

## Slide 39: SourceLink + Sercel 428 & JOVC
Integration of SourceLink/UE2/Force3 with a Sercel 428 JOVC (+Navigation Patch) recording system.
Enables Source Driven acquisition in Flip-Flop or Ping-Pong mode of two or more fleets.
Integrated Operation Process:
  Vibrator sends Ready Message
  SourceLink reports source COG position to Sercel
  Sercel picks the nearest Source Point and waits for timebreak
  SourceLink starts Vibrators and sends timebreak and QC to Sercel

## Slide 40: SourceLink + Sercel
Use SourceLink/UE2/Force3 while the 428 recording system records data in microseismic mode.
Enables SourceLink to perform any regular vibroseis or HPV mode including: Slip Sweep, HFVS, ISS and DSS, etc.
Serce 428 runs in microseismic mode, all channels are continuously recording.
SourceLink has total control of sources, shot selection and firing.
Live spread is calculated later, during the data harvest and processing stage.

## Slide 41: Nodal Systems
SourceLink Provides a comprehensive solution for all nodal systems

## Slide 42: Nodal Systems
Source control and acquisition coordination front-end

## Slide 43: Nodal Systems
Tailor made reports for each supported nodal recorder for easy transcribing

## Slide 44: Nodal Systems
Node location and status import for visualization

## Slide 45: Nodal Systems
Node Deployment Location on GIS map with quick access to status

## Slide 46: Nodal Systems
Easy way to check if a line is fully deployed

## Slide 47: Nodal Systems
Sortable and Filterable grid view of all node status

## Slide 48: Nodal Systems
Active Spread check before each shot point start

## Slide 49
HPV Building Blocks
Force3
▪ Start on GPS Time
▪ Start via VHF/WiFi
▪ Internal (PSS, VSS, QC)
▪ USB (PSS, VSS, QC)
UE2
▪ Analog Aux Out
▪ Digital Aux Storage
▪ Interface to Ext Rec Sys
Mesh WiFi
▪ Auto Setup
▪ Start via WiFi
▪ Group Messages
  ▪ Redundancy
  ▪ +Production
Analog VHF
▪ Start via VHF
▪ Narrow Band
▪ Legal in Most Countries
▪ Repeaters Easily Added
GPS
▪ Start on GPS
▪ GPS Time & Position
▪ Stakeless Surveys
Digital VHF
▪ Start via VHF
▪ High Speed
▪ Narrow Band
▪ Legal in Most Countries
▪ Repeaters Easily Added
Navigator
▪ F3 Integration
▪ Stakeless Surveys
▪ Shows Acquired Shots
SourceLink
▪ Setup (SP1/SPS,UE2,F3)
▪ Fire Shots (via UE2 or F3)
▪ QC Shots (via UE2 or F3)
▪ QC Safety & Permit Issues
▪ Extensive Reports

## Slide 50
TDMA Analog Radio Mode
Standard VHF radios
Eliminates radio collisions
Starts on GPS time
Optimized for HPV modes
Radio Repeaters do not change start time
Analog Radio similarities
Zero Overhead – Improved Production Rates
Analog Radio Mode
Standard VHF radios
Standard Start codes
Compatible with older source controllers
Digital Radio Mode
Start on GPS time
Eliminates radio collisions
Optimized for HPV modes
Radio Modes

## Slide 51
T1: Analog Start Code
T2: Group 1 Sweep
T3: Group 1 Listen
T4: V1 PSS
T5: V2 PSS
T6: Analog Start Code
T7: Group 1 Sweep
T8: Group 1 Listen
T9: V3 PSS
T10: V4 PSS
Conventional
Truck
V2
V1
V4
V3
Start on analog VHF Synchronization ( Analog VHF radios)
PSS returns in time slots at end of sweep
All Radio Traffic on single frequency
Radio collisions prevents or slows down many high production vibroseis techniques
Allows Flip/Flop (Ping Pong) HPV mode
VHF radios similarities ( independent timing and QC)
VHF synch and GPS time synch comparison ( verifies GPS time is accurate)
Central SourceLink software controls HPV operation based on HPV rules
T1
T2
T3
T4
T5
T6
T7
T8
T9
T10

## Slide 52
GPS Starts
Truck
T1: Start on GPS Time
T2: Poll PSS
T3: Poll PSS
T4: Poll PSS

## Slide 53
Polling
Truck
T1: Start on GPS Time
T2: Poll PSS
T3: Poll PSS
T4: Poll PSS

## Slide 54
Group WiFi
Truck
T1: Start on GPS Time
T2: Poll Group PSS
Start on GPS Time
Poll PSS

## Slide 55
Multiple Encoders / Frequencies
Truck
T1: Start on GPS Time
T1: Poll Group PSS
Start on GPS Time
Poll PSS

## Slide 56
T0: Start on GPS Time
T1: Poll PSS
Distributed Acquisition (ISS/DSS)
Truck
T1: Poll Group1 PSS
T2: Poll Group2 PSS
T0: Start on GPS Time
T1: Poll PSS

## Slide 57
Autonomous Acquisition
T0: Start on GPS Time
T1: Poll PSS
T0: Poll PSS
T1: Start on GPS Time

## Slide 58
Collaborative Acquisition
Truck
SourceLink Sync
DVHF Far: ISS/DSSS
DVHF Near: SlipSweep
No DVHF: GPS TimeSlot

## Slide 59
Communications
  VHF Radio between UE2 and Groups
  MESH WiFi between Each Vibrator for Easy Setup
Intra Vib Communications
  Provides reception redundancy
  Reduces missed Sweeps
  Display all Vibs in group accurately in each Vib
Allows Group messaging
  COG “Group” Ready messages
  Compound PSS messages
  Reduced radio traffic
Force III – WiFi Vib Group Comms
Mesh
WiFi
Mesh
WiFi
Mesh
WiFi
Mesh
WiFi
Fleet 1
Fleet n
Fleet n+1
Fleet n < 256

## Slide 60
Access every Force3 in the group over WiFi from your vehicle
Receive PSS from every Force3 in the group
Real-Time Quality Control
  Signature Data
  Vib QC Data
Upload Parameters
  Sweep Table
  Vib Parameters
Wireless Digital Similarities
Upload Firmware
Upload Custom Sweeps
Force III – WiFi Vib Mechanic
Mesh
WiFi

## Slide 61
Central Shooting VS QC
Central Shooting
Requires Radio Communications
  All Fleets
  All Times
Limited By Radio
  Bandwidth
  Latency
  Uptime
Central QC
Radio Not Required
At All Times
Lack Of Radio Does
Not Stop Production
Synchronizes Status
When Radio Working

## Slide 62
Fully compatible, accurate, reliable and safe control of all servo-hydraulic vibrators
Works with previous generation controllers
Maximum Force output with minimum distortion
Force III Vibrator Controller (F3)
Notes: Force 3 vibrator decoder is in the vibrator. It generates the sweep for the vibrator, and controls how that sweep is applied to the ground.

## Slide 63
F3 uses stable Force and Phase control for accurate and reliable control of all vibrators
Limits control allows broad band sweeps without any worry of damaging the vibrator
Force III - Performance

## Slide 64
Sweeps from 0 to 700 Hz have been tested
64 standard, custom or linked sweeps
Non-Linear sweeps can be used to increase energy at desired frequencies
Random sweeps and Adaptive LMS Digital Filter control option available
High definition stored sweep support
Force III - Sweeps

## Slide 65
Internally stored location and performance info for each shot for redundancy (PSS, VSS & QC)
Store PSS, VSS & QC on USB for easy harvesting
Force III – Storage
Notes: Force 3 vibrator decoder is in the vibrator. It generates the sweep for the vibrator, and controls how that sweep is applied to the ground.

## Slide 66
Internal 32 bit A/D Vibrator Signature Recorder: Vibrator Reference, Baseplate, Reaction Mass, Ground Force along with GPS Time and GPS Position are stored internally for each sweep.
All Vibrator signatures for a VP can be combined
Analog Vibrator signatures available for external recording
User selectable Sample Rate (¼ms to 8ms)
Force III – Signature Recording

## Slide 67
Enables vibrator technician to see real time vibrator signature data (TR, SBP, SRM, SGF)
Force III – Standard VSS

## Slide 68
QC vibrator performance in the field, using independent accelerometers
  Amplitude and phase displays
  Force and distortion analysis
  Verifies correct ground force calculation and polarity
Includes "Vibrator QC Software" for Vibrator Analysis
  Time and Frequency Domain Tests
  Measures Output Force and Phase Error
  Measures Distortion and Start Time Differences
BirdDog 3 – Vibrator QC
Notes: This is the follow-up the previous slides. This is an independent QC system for all vibroseis units!

## Slide 69
Additional functionality than BirdDog 3-3
Check Zero Time for up to 10 Vibrators at a time
Connect directly to the Vibrator Decoder to test all QC Signals
Independent Magnetic Accelerometers (up to 8)
Built-In Wireline Sims for up to 5 Vibrators
Test Accelerometers
BirdDog 3-11 – Vibrator QC
Notes: This is the follow-up the previous slides. This is an independent QC system for all vibroseis units!

## Slide 70
VibTest + BD3-11 – Vibrator QC

## Slide 71
Uses independent accelerometers to approximate the Ground Force using the Weighted Sum method.
Measures the Hold Down weight and the Output Force of the Servo Hydraulic Vibrator unit.
The output of the Load Cells can be recorded with any accurate seismic recording system.
Load Cell – Vibrator QC
Notes: This is the follow-up the previous slides. This is an independent QC system for all vibroseis units!

## Slide 72: Navigator Software
Vibrator Navigation for stake free operation
Simple Go-To Flag Navigation
Shows all vibrators in a Group
Computes distance to Flags
Keep out zones
Easy to see ‘Track’ of previous positions or planned trail

## Slide 73: Navigator Features
Scouting Feature - Routes and Trails can be recorded and loaded for “drive around” guidance
Map overlay, source and receiver points, shape files, and user edited feature layers may be easily loaded and turned on or off to enhance readability of display

## Slide 74: Navigator Integration
Optimized for use with UE2 / Force 3 system
Shows Shot Points Remaining to be acquired
Wireless connection to GPS Data
Uses same high accuracy GPS used for vib control electronics
SourceLink observer commands next waypoint to Navigator software

## Slide 75: Tracking Software
Specifically Designed for Seismic Industry
Loads Standard Seismic Surveying Files (SEG P1)
GeoFencing with Buffer Zone
Vehicle Paths and Routes
Multiple Layers – Easily selected for display

## Slide 76: Tracking – Alerts
Legal
Keep Out Area Alerts
Restricted Area Alerts
Warnings Buffers for keep out and restricted areas
Verification of vehicle positions during entire job.
Safety
Speed Warning Alerts
Idle Alerts
Hazards Alerts

## Slide 77: Tracking – Journeyman Reports
Near Source or Receiver
Journeyman report creation on Time interval (30 minute default)

## Slide 78: Tracking – KML / KMZ Reports
Standard Google Earth Report
Crew operation is easily monitored from office (auto FTP files to server)
Alert Only reports can be generated
Real Time Viewing
Can view History of each vehicle or all vehicles

## Slide 79: Tracking – Remote Monitoring
VHF Radio with GPS used in all vehicles and carried by Juggies
VHF Radio is used for Voice commands. GPS position is sent in the background and not heard by anyone.
Central Recorder and Office can receive the data via VHF radio link, or can download the data when the unit is close to the office.
The Tracker program on the Office computer or in the Central Recorder is also connected to the Internet.
The Tracker program uploads the data via FTP to a central server.
This data can then be viewed by the Safety Officer, Crew supervisor or even by the Client.

## Slide 80
Seismic Source Company is a manufacturer of seismic instruments and data acquisition systems. Its products are used in a broad range of applications: Seismology, Structural Monitoring, Seismic Site Evaluation, Civil Engineering, Gas and Oil Exploration, and Industrial Vibration Monitoring.
Seismic Source Company
Seismic Source Company
Ponca City, Oklahoma
(580) 762-8233
www.SeismicSource.Com
Notes: Filler slide to leave up on the screen while you’re answering questions, etc.
Enjoy!